## KZ440A-LTD (1982)

| Horsepower 40 hp @ 8500 rpm | Torque 3.6 kg-m /26 lb ft @ 7k | Turning Radius 2.4 m / 7' 10-1/2" | Braking Distance 44.3' from 31 mph |
| --- | --- | --- | --- |
| Overall Length 2.08 m / 81.9" | Overall Width .81 m / 31.9" | Overall Height 1.18 m / 46.5" | Wheelbase 1.39 m / 54.7" |
| Road Clearance 14 cm / 5.5" | Dry Weight 169 kg / 373 lbs | Engine Type 4-stroke, SOHC, 2-cylinder, air-cooled | Displacement 443 cc / 27.02 cid |
| Bore & Stroke 67.5 x 62 mm / 2.65 x 2.44" | Compression Ratio 9.2/1 | Starter Electric | Carburetors 2 Keihin CV36mm |
| Ignition System Battery & Coil, electronic | Ignition Timing 10� BTDC @ 1200 ~35� BTDC @ 3200 | Plugs NGK B7ES or ND W22ES-U | Engine Oil SAE 10W-40, 10W-50, 20W-40, 20W-50 API SE* |
| Oil Capacity 2.9 litres / 3.1 US Qt | Transmission Type 6-speed, constant mesh, return shift (1 dn /5 up) | Clutch Type Wet, multi-plate | Primary Ratio 2.43:1 (56/23) |
| Final Drive Ratio 3.0/1 (45/15) | 1st Gear 2.54/1 (33/13) | 2nd Gear 1.75/1 (28/16) | 3rd Gear 1.32/1 (25/19) |
| 4th Gear 1.10/1 (23/21) | 5th Gear 0.96/1 (22/23) | 6th Gear 0.88/1 (21/24) | Castor 27.5� |
| Trail 112 mm / 4.4" | Front Tire 3.25S-19 4PR / 100/90-19 | Rear Tire 130/90-16 67S | Fuel Capacity 12 litres / 3.1 US Gal |
| Battery 12V 12AH | Headlight 12V 50/35W | Tail/Brake Light 12V 8/27W | Turn Signal Lights 12V 23W |
| Gauge/Indicator Lights 12V 3.4W | Horn 12V 2.5A | Fuses 20A (main) 10A (head/tail) | Brakes 11" single-piston (front) mechanical drum (rear) |
| Fork 33 mm air assisted | Shock Absorbers 2 13", manual adj | Chain 530-104 HD** | Fuel 87 Octane R+M/2 91 Octane Research*** |
| Intake Valve**** .17~.22mm .007~.009" | Exhaust Valve**** .17~.22mm .007~.009" | Points (if equipped) 0.3~0.4mm 0.12~0.16" | Cam Chain Adjust automatic |

*Current Kawasaki 4-Cycle oil is API SJ, SH rated. The use of SJ rated automobile oil is not recommended in a motorcycle.

**Original equipment was an EK530D-G non-O-ring chain. An O-ring chain can be retrofitted. Always replace both sprockets when replacing the chain.

***Not normally encountered in the United States.

****Screw and locknut adjustable. Adjust cold.