Exhaust Insulating Wrap

Note: It takes more material than you think so I wrap the pipe loosely and add about ten feet to cover one pipe. You never want to come up short

It’s a simple operation so Larry started by laying out everything that you will need(except the rubber gloves), water spray bottle, high heat paint (for the area left un- wrapped), stainless steel safety wire and Thermo-Tec insulating wrap.

Looks like you can buy this at any hot rod shop or Pep Boys.

Take 1 full wrap and secure it with safety wire (position so as not to show with next wrap, (insert through the wrap and twist wire tight). Use gloves because wrap is impregnated with graphite and contains fiberglass. It can make a big uncomfortable mess.

Continue to wrap, overlapping ½ of the last wrap with each turn. Spray the material lightly with water to help it conform to the shape of the pipe.

The wet wrap slipping over a mounting stud.

If you wet it down really good, it is very easy to push mounting studs through the wrap.

Tie the finished wrap with a double wrap of safety wire, or you can use hose clamps. Larry starts wrapping from the end of the pipe, so the leading edge is not exposed and is clean as possible.

Lightly wet the entire pipe and "wring" (massage it), it to make the wrapping mold to the pipe. Set the pipe aside and let it air dry.

Four hands are better than two. Have a friend help for a tighter wrap.

Here’s the finished pipes. Let them air dry and install the bastards.

Note: this stuff must cure, when you start up the first time, it’s going to smoke and smell real bad. Let your scooter run a few minutes and shut it down. I prefer to cure it (let it set and cool) and then get in the wind to finish the curing process. Due to higher exhaust velocity, it is advised to check the jetting after you run it. You can go leaner with the wrap.

Ah the shop babe, Abbey. Yeah, yeah, that’s a Larry built bike with wrapped pipes. He built this bike in 127 hours for a dealer show.

Larry Curik 
Lone Star Choppers, Inc. 
(618) 406-1554 
Larry@lonestarchoppers.com 
Lonestarchoppers.com 
7858 Andy Road 
Waterloo, Illinois 62298