Exhaust Smokes Excessively:

White smoke:

Piston oil ring worn 
Cylinder worn 
Valve oil seal damaged 
Valve guide worn 
Engine oil level too high

Black smoke:

Air cleaner clogged 
Main jet too large or fallen off 
Starter plunger stuck open 
Fuel level in carburetor float chamber too high

Brown smoke:

Main jet too small 
Fuel level in carburetor float chamber too low 
Surge tank duct loose 
Air cleaner poorly sealed or missing