Engine Doesn't Start, Starting Difficulty

Starter motor not rotating:

Starter lockout or neutral switch trouble 
Starter motor trouble 
Battery voltage low 
Relays not contacting or operating 
Starter button not contacting 
Wiring open or shorted 
Ignition switch trouble 
Engine stop switch trouble 
Fuse blown

Starter motor rotating but engine doesn't turn over:

Starter clutch trouble

Engine won't turn over:

Valve seizure 
Cylinder, piston seizure 
Connecting rod small end seizure 
Connecting rod big end seizure 
Transmission gear or bearing seizure 
Camshaft seizure 
Balancer bearing seizure

No fuel flow:

Fuel tap vacuum hose clogged 
Fuel tank air vent obstructed 
Fuel tap clogged 
Fuel line clogged 
Float valve clogged

Engine flooded:

Fuel level in carburetor float bowl too high 
Float valve worn or stuck open 
Starting technique faulty 
(When flooded, crank the engine with the throttle fully open to allow more air to reach the engine)

No spark; spark weak:

Battery voltage low 
Spark plug dirty, broken, or maladjusted 
Spark plug cap or high tension wiring trouble 
Spark plug cap not in good contact 
Spark plug incorrect 
IC ignitor trouble 
Neutral, starter lockout, or side stand switch trouble 
Pickup coil trouble 
Ignition coil trouble 
Ignition or engine stop switch shorted 
Wiring shorted or open 
Fuse blown

Compression low:

Spark plug loose 
Cylinder head not sufficiently tightened down 
Cylinder, piston worn 
Piston ring bad (worn, weak, broken, or sticking) 
Piston ring/land clearance excessive 
Cylinder head gasket damaged 
Cylinder head warped 
Valve spring broken or weak 
Valve not seating properly (valve bent, worn, or carbon accumulation on the seating surface) 
Hydraulic lash adjuster damaged (worn, seizure, or spring broken) 
Hydraulic lash adjuster oil passage clogged