Used Bike Checklist

Used Bike Checklist

This check list might be a bit rigid, but it should cover most issues.

Øverst i skjemaet

Front End:
No play in head bearings
Triple clamp bolts tight
Inner fork tubes smooth and unrusted
Slider dust seals intact
Fork seals intact and not leaking
Wheel bearings sound and correctly lubricated
No excessive play in fork
Brakes do not bind
Brake shoes/pads not worn out
Caliper(s) do(es) not leak
Brake lines/cables in good condition
Master cylinder does not leak
Brake fluid is not contaminated
Front wheel runs true*
Brake rotor(s) true and within specs
Handlebar or clip-ons tight and undamaged
Control levers are not bent
Grip do not show abrasion damage on ends
Turn signal lenses intact and signals work

Rear End:
Wheel bearings undamaged
Brakes do not bind
Brake shoes/pads are not worn out
Rear wheel is true*
Sprocket tight and teeth undamaged
Chain correctly adjusted
Chain is not excessively worn, rusted, or binding
Turn signal lenses intact and signals work
Turn signals do not show signs of abrasion wear**
Brake light lense intact and brake light works with both foot and hand brake
Rear wheel properly aligned
No lateral play in swing arm
Shocks are in good condition, not leaking, and springs do not sag

Tires:
Tires are correct size
There is adequate tread on both tires
No checking or cracking on sidewalls
No "fix-a-flat" type repair goop inside tire
Tire is no more than 3 years old
No plugs in tubeless tires
Tubes have not been patched***
Tires are correct speed and load rating for motorcycle
Tires are properly inflated
Rear tire is not squared off
No ArmourAll® or similar product has been used on tires

Frame:
No bent frame members
Frame paint is intact and there are no rusted areas
All attachment points and welds are sound

Gas Tank:
Paint undamaged
No rust on or in tank
Petcock functions correctly
Nothing leaks
Filler cap is present and tight
Tank mounts are sound

Engine and Transmission:
No obvious leaks
Oil is correct type and filled to correct level
Air filter clean and tight
Valves correctly adjusted
Cam chain properly tensioned
Points & condenser correct, if present
Correct spark plugs/plugs in good condition
Engine turns over easily
Idle speed correct
No loose bearings
Compression and leak down test within specs
No excessive gear noise
Cannot be shifted above 1st gear when stationary
Shifts smoothly and without binding or missing shifts
If separate transmission, is filled with proper lubricant to correct level
Carburator(s) adjusted correctly

Exhaust System:
No leaks
Muffler baffles have not be removed and any packing is present
Exhaust system is not marked "race only"
No abrasion on outside of pipes or mufflers**

General:
All fasteners, screws, nuts, bolts, etc., are tight
Paperwork is in order
Engine and chassis serial numbers match (non matching numbers may indicate a replaced engine) ***

* This is particularly important with cast wheels, for while a spoked wheel can be trued up by a  competent mechanic as long as the rim isn't bent, an out of true cast wheel will have to be replaced. Cast motorcycle wheels generally cost at least $350.00 each. 

** Generally a sign that the bike has been dropped.

 *** None of the 400/440 had matching numbers from the factory.

BY JACK MCDANIEL